## Slide 1: Microprocessors and Assembly Language Lecture 18 Hamed Farbeh farbeh@aut.ac.ir Fall 2022

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
  Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013.

## Slide 3: Instruction Formation of the ARM

## Slide 4: Instruction Formation
General formation of data processing instructions
Cond [31:28]: Condition field (will be discussed in Ch. 4)
[27:26]: Always “00”
I [25]: Defines the type of second operand
    I = 1: Op2 is an immediate value
[24:21]: Opcode
S [20]: Update CPSR

## Slide 5: Instruction Formation
ADD instruction format
SUB instruction format
Branch (B) instruction format

## Slide 6: Little Endian vs. Big Endian War
Little endian
  Low byte goes to the low memory location
  High byte goes to the high memory address
  All Intel processors
Big endian
  Low byte goes to the high memory location
  High byte goes to the low memory address
  Freescale (formerly Motorola and now NXP)
ARM allows the software designer to choose!
  A hardware switch that is controlled by software

## Slide 7: More Example for Little endian & Big Endian
4F52 in little endian:
52 is stored at storage address 1000
and 4F is stored at 1001
4F52 in big endian:
4F is stored at storage address 1000
and 52 is stored at 1001
Value | Address
4F | 1001
52 | 1000
Value | Address
52 | 1001
4F | 1000

## Slide 8: Some ARM Addressing Modes

## Slide 9: Addressing Modes
Addressing Mode
  The various ways operands are specified in the instruction
  Is the way CPU generates address from instruction to read/write the operands
Three basic modes
  Register
  Immediate
  Register indirect (indexed addressing mode)

## Slide 10: Addressing Modes
Register Addressing Mode
Immediate addressing mode
Register Indirect addressing mode (Indexed)

## Slide 11: Addressing Modes
Register Indirect addressing mode (Indexed)
  Can be used for pointer implementation
    char *ourPointer; ourPointer = (char*) 0x12456; //Point to location 12456 *ourPointer = 25; //store 25 in location 0x12456 ourPointer ++; //point to next location
        LDR R2, =0x12456 ; point to location 0x12456 MOV R0, #25 ; R0 = 25 STRB R0, [R2] ; store R0 in location 0x12456 ADD R2, R2, #1 ; increment R2 to point to next location

## Slide 12: Example
MyString DCB “Hello world!”, 0
AREA MyCode, CODE, READONLY
    ENTRY
    LDR R0, =MyString
    mov R1, #0
LoopCount
    LDRB R2, [R0], #1
    CBZ R2, Here
    ADD R0,#1
    ADD R1,#1
    B LoopCount
Here B Here
END

## Slide 13: End of Chapter 2!