## Slide 1: Microprocessors and Assembly Language Lecture 25 Hamed Farbeh farbeh@aut.ac.ir Fall 2022

## Slide 2: Copyright Notice
Parts (text & figures) of this lecture are adopted from:
Arm Assembly Language Programming and Architecture, Volume 1, 1st edition, Muhammad Ali Mazidi, Sarmad Naimi, and Sepehr Naimi, MicroDigitalEd, 2013

## Slide 3: Appendix E: Passing Arguments into Functions

## Slide 4: Passing Arguments
High level languages
  Call a function with the specified arguments
Assembly
  Branch to another part of the code
  How are arguments passed?
Three ways to pass arguments (parameters) to functions
  Through registers
  Through memory using references
  Using stack

## Slide 5: Passing Arguments
Through Registers
            AREA OUR_PROG, CODE, READONLY MOV R0, #5 ; R0 = 5 MOV R1, #7 ; R1 = 7 BL BIGGER ; BIGGER(5, 7) HERE B HERE ; stay here ;---------------------------------------------------------------------
            ; BIGGER returns the bigger value
            ; Parameters: R0 and R1: the values to be compared ; Returns: R0: containing the bigger value
            ;--------------------------------------------------------------------- BIGGER CMP R0, R1 BHI L1 ; if R0 > R1 go to L1 MOV R0, R1 ; R0 = R1 L1 BX LR ; return END

## Slide 6: Passing Arguments
Through memory using references
  Store the data in memory and pass its address through a register
      ADR R0, OUR_STR ; R0 = addr. of OUR_STR
      BL STR_LENGTH ; STR_LENGTH(&OUR_STR)
      HERE B HERE ; stay here
      OUR_STR DCB "HELLO!“
      ; ----------------------------------------------------------------------
      STR_LENGTH MOV R1, R0 ; move string pointer to R1
      MOV R0, #0 ; use R0 as string length counter
      L_BEGIN LDRB R2, [R1] ; fetch a character from string
      CMP R2, #0
      BXEQ LR ; return if character is null (end of string)
      ADD R1, R1, #1 ; point to next character in string
      ADD R0, R0, #1 ; increment the counter
      B L_BEGIN

## Slide 7: Passing Arguments
Through stack: The arguments are pushed onto the stack just before calling the function and popped off after returning
    LDR SP, =(0x40000000+(16*1024)) ; init stack pointer
    MOV R0, #5
    PUSH {R0} ; push Arg1
    MOV R0, #7
    PUSH {R0} ; push Arg2
    BL BIGGER ; BIGGER(5, 7)
    ADD SP, SP, #8 ; adjust the stack pointer to remove the arguments
    HERE B HERE ; stay here
    BIGGER
    LDR R0, [SP, #4] ; R0 = arg1
    LDR R1, [SP, #0] ; R1 = arg2
    CMP R0, R1
    MOVLO R0, R1 ; if R0 < R1 move R1 into R0
    L1 BX LR ; return

## Slide 8: Passing Arguments
For the program to work correctly, both the calling code and the called code must use the same method of passing arguments
This is called the ABI (Application Binary Interface) or the Calling Convention
What if you’re using a library, written by another person?
Need a standard that everyone abides by
In ARM CPU:
  If there are four or fewer arguments:
    The arguments are passed in the first four registers
  If there are more than four arguments:
    The first four are passed in the first four registers
    The rest are passed on the stack

## Slide 9: ARM Application Procedure Call Standard
AAPCS provides a standard for implementing the functions
Some rules
  The arguments must be sent through R0 to R3
  The return value must be returned in R0 (and R1 for return a 64-bit)
  The functions can use R4 to R8, R10 and R11 for temporary storage
    Their values must be saved upon entering the function and restored before returning
  The stack must be used as Full Descending

## Slide 10: ARM Application Procedure Call Standard
Register | Role | Saved by
R0 | Argument / Result | Caller
R1 | Argument / Result | Caller
R2 | Argument | Caller
R3 | Argument | Caller
R4 | Variable | Callee
R5 | Variable | Callee
R6 | Variable | Callee
R7 | Variable | Callee
R8 | Variable | Callee
R9 | Platform Register | Depends on the platform
R10 | Variable | Callee
R11 | Variable | Callee
R12 | Intra-Procedure-Call Scratch Register | Caller
R13 / SP | Stack Pointer | Special Purpose
R14 / LR | Link Register | Special Purpose
R15 / PC | Program Counter | Special Purpose

## Slide 11: Question
Write two subroutines ‘quickSort’ and ‘partition’ that does the quick sort algorithm in ARM Assembly using AAPCS conventions.

## Slide 12: The End!